IPOCS
Revision log
Revision	Date	Description of changes
1.0	2017-01-05	First version

Table of Contents
# EXECUTIVE SUMMARY
## Purpose
This document defines the communication interface between the central system and the distributed object controller system (OCS).
This specification is loosely based on the FFFIS TCC-OCS specification for ERTMS-R (Level 3) systems.
## Scope
The specification deals with all aspects of the communication interface. However, a few options are identified as selectable. To fully specify the interface for a specific application, all such options must also be specified.
# REFERENCE DOCUMENTS
Id	Title	Doc ID, Version	Date	Author
[1]	Safety related communication in closed transmission systems	CENELEC EN 50159-1	March 2001	CENELEC
[2]	Safety related communication in open transmission systems	CENELEC EN 50159-2	March 2001	CENELEC
[3]	ERTMS-R System Requirements Specification	ERTMS-R 07004		BV
[4]	Safe Transmission Protocol – STSAP	3NSS004700D0104		Bombardier
[5]	Internet Protocol	RFC 791	Sept. 1981	IETF
[6]	Transmission Control Protocol	RFC 793	Sept. 1981	IETF
[7]	User Datagram Protocol	RFC 768	August 1980	IETF
[8]	ERTMS/ETCS Class 1 / System Requirement Specification	SUBSET-026 / Version 2.3.0	2006-02-24	UNISIG
[9]	ERTMS/ETCS Class 1 / RBC Safe Communication Interface / Requirements	SUBSET-097 / Version 1.1.0	2005-06-14	UNISIG
[10]	Euroradio FIS	SUBSET-037 / Version 2.2.5	July 2003	UNISIG

# DEFINITIONS AND ABBREVIATIONS
## Abbreviations
Term	System Requirements Specification
CENELEC	Comité Européen de Normalisation Electrotechnique
CRC	Cyclic Redundancy Check
CRCC	Cyclic Redundancy Check Code
DHCP	Dynamic Host Configuration Protocol
ERTMS	European Rail Traffic Management System
ETCS	European Train Control System
HTTPS	Hyper Text Transfer Protocol Secure
IL	Interlocking
IP	Internet Protocol
OC	Object Controller
OCS	Object Controller System
RAMS	Reliability, Availability, Maintainability and Safety
RBC	Radio Block Centre
SRS	System Requirements Specification
SFTP	Secure File Transport Protocol
SSH	Secure Shell
TCC	Traffic Control Centre

## Definitions
Application layer	The application layer is the seventh level of the seven-layer OSI model. It interfaces directly to and performs common application services for the application processes
Data link layer	At this layer, data packets are encoded and decoded into bits. It furnishes transmission protocol knowledge and management and handles errors in the physical layer, flow control and frame synchronization
Network layer	This layer provides switching and routing technologies, creating logical paths for transmitting data from node to node. Routing and forwarding are functions of this layer, as well as addressing, internetworking, error handling, congestion control and packet sequencing
Physical layer	This layer conveys the bit stream - electrical impulse, light or radio signal -- through the network at the electrical and mechanical level. It provides the hardware means of sending and receiving data on a carrier, including defining cables, cards and physical aspects
Routing	Routing is the technique by which data finds its way from one host computer to another
Telnet	Protocol for remote log in over TCP/IP
Transport layer	This layer provides transparent transfer of data between end systems, or hosts, and is responsible for end-to-end error recovery and flow control. It ensures complete data transfer

# VERSION MANAGEMENT
## Application Protocol
The revision identity of this protocol specification consists of two numbers:
The major number, which reflects the application protocol version number, i.e. implementations with the same protocol version number must be functionally and layout-wise compatible (see 6.2)
The minor number, which denotes changes which are not relevant to the behaviour of the application protocol.
# LOWER PROTOCOL LAYERS
## Physical Layer
The physical layer defines all electrical and physical specifications for devices.
This includes the layout of pins (connectors), voltages, and cable specifications.
Connection interface in this layer is Ethernet based with a RJ-45 connector.
## Network Layer
IP shall be used as network layer protocol. See ref. [5].
## Transport Layer
TCP (ref. [6]) should be used as transport layer protocol, as it provides CRC checks and guarantees delivery as well as in order delivery.
If any other protocol is used, it is up to the implementation to add these functions or make sure that the other transport layer provides it as well.

# APPLICATION PROTOCOL
## Protocol Components
This chapter describes the message format used in the application protocol. Format is described by three components: Message, Packet and Variable.
A Message consists of a header and one or more Packets. The header and the packets are composed from Variables.
The layout of the application protocol PDU shall be as follows:
Header	1st packet	2nd pkt (optional)	nth pkt

Figure 6.1‑1: Layout of the Application Protocol PDU
### Definition of Variables and rules for variable coding
Variables shall be used to encode single data values. Variables cannot be split in minor units. The whole variable has one type (meaning).
Variables may have special values, which are related to the basic meaning of the variable.
Names of variables are unique. A variable is used in context with the meaning as described in the variable definition. Variables with different meanings have different names.
Signed values shall be encoded as 2’s complement.
When transmitting, the most significant byte shall be transmitted first (network byte order).
All Variables have one of the following prefixes:
RL_	Length
RM_	Miscellaneous
RN_	Number
RNID_	Identity Number
RQ_	Qualifier
RT_	Time/Date
RX_	Text string
RXID_	Identity string

All variables are listed in alphabetical order in section 8.
Length of variables is given in bytes.
Text variables (RX_... and RXID_...) have variable length, and shall be terminated by a null byte (value 0). Embedded null bytes are not allowed.
### Definition of Packets and rules for packets handling
Packets are multiple variables grouped into a single unit, with a defined internal structure.
This structure consists of a unique packet number, the length of the packet in bytes and an information section containing a defined set of variables. The packet structure is defined as follows:
Variable	Length	Comment
RNID_PACKET	1	Packet identifier (see section 7.1 )
RL_PACKET	1	Packet length (N + 3)
RM_ACK	1	Packet instance identity for acknowledge
Other variables in packet if any	N	Refer to packet definition in section 6.5

The data element transmission order shall respect the order of data elements listed in the packet definition (from top to bottom).
The packet length in RL_PACKET shall be the length in number of bytes of the whole packet.
The variable RM_ACK contains a numerical identification of the packet instance, to be used when returning an Acknowledgement Package (see 6.3). A value of 0 indicates that no acknowledgement is expected.
All packets are listed in section 7.
### Definition of a message and rules for message handling
A message is the whole application data transmitted at a given time on the interface between TCC and a distributed unit. The message shall have the following format:
Variable	Length	Comment	Format
RL_MESSAGE	1	Message length	The massage length shall be the length in number of bytes of the whole message. / The total length of a message must not exceed the capabilities of the receiving unit.
RXID_OBJECT	Variable	Identity of object unit (see section 6.1.3.1)	Messages shall be treated by the receiver in the order of their reception.
First Packet	Variable		The message body shall consist of one or more packets (see 6.1.2). / Some packets and its variables in the connection management section are constant, i.e. protocol version independent.
Other packets, if any	Variable		.

#### Unit Identification
Each object shall have a unique identity, to be included in each message header (RXID_OBJECT). The TCC does not need a name.
The identity consists of a null terminated UTF-8 string and must be unique in the system so that no naming collisions occur.
## Connection Procedure
Communication is always initiated from the distributed units. This makes TCC independent of unit IP addresses, allowing for DHCP or similar techniques to be used in the distributed system, as well as fixed IP addresses.
On power up, the distributed unit
- Initialises connection procedure in lower protocol layers
- Sends a Connection Request Packet (7.2.1)
- Waits for a Connection Response Packet (7.2.2)
While no response is received, connection attempts are repeated at a configurable interval.
The exchanged packages contain protocol version information. (see 4.1) Both communication partners have to verify the local node protocol version to be used according to the following rules:
- If the local node protocol version is the same as the remote node protocol version, then the communication is allowed.
- If the local node protocol version is lower than the remote node protocol version, then the decision whether the connection is allowed, and control of it, is the responsibility of the remote node ‑ communication is allowed from the local node.
- If the local node protocol version is higher than the remote node protocol version, then the local node has to decide whether the communication should be established. For this reason each node has to know exactly to which versions it is compatible.
If either side decides not to establish communication, it sends a Disconnect Packet (7.2.3).
The following figure shows a successful connection procedure.

Figure 6.2‑1: Connection procedure
The following figure shows an unsuccessful connection procedure (TCC does not accept protocol version of OC).

Figure 6.2‑2: Connection procedure

The procedure described above, and the layout of the packets involved, must not be changed in subsequent versions of this protocol.
The Connection Request Packet contains the version identity of the active site data in the distributed unit. If the received version identity is incorrect, TCC will send a Disconnect Packet indicating this. The distributed unit may then initiate downloading of the correct site data (outside of this protocol), so that subsequent connection attempts will be successful.
When communication is established, current status of all controllers and objects where status information is available, is sent to TCC.
## Message Exchange and Acknowledgement
Once communication is established, either party may send packets at any time.
Many packets will require an acknowledgement from the receiving application. The RM_ACK variable in the packet is used for this purpose.
If acknowledgement is expected, the sender places a unique identity in the RM_ACK field, which will distinguish this packet instance from other packets to the same receiver. The receiver returns the same RM_ACK value in an Acknowledgement Packet (7.2.4), together with a code indicating acceptance or reason for rejection.
Action to be taken by the application if acknowledgement is not received within the expected time is implementation specific, and will not be specified here.
To be able to use retransmission of the packet as an action, applications must follow these rules:
- A sender, which intends to use retransmission, shall ensure that only one unacknowledged packet to the same receiver exists at the same time
- All senders shall ensure that RM_ACK in a new message is not identical to the latest non-zero RM_ACK to the same receiver
- All receivers shall recognise a retransmission of the latest acknowledged packet from the same sender (identical RM_ACK), and respond by repeating the acknowledgement Packet. No action shall be taken on account of the contents of the received packet
If acknowledgement is not required, the sender sets RM_ACK to 0.
The following figure shows message exchange procedure with and without acknowledgement. Message is from distributed unit to TCC, but the procedure is identical in the opposite direction.

Figure 6.3‑1: Message exchange
## Disconnection
Either party may disconnect at any time, by requesting disconnection from the lower protocol layers. The reason for this would normally be to force rerouting through an alternative connection path.
It is also possible to actively request disconnection by sending a Disconnect packet (7.2.3).
On reception of a Disconnect packet, the receiver requests disconnection by the lower protocol layers.
When disconnection is reported from the safety layer in a distributed unit, spontaneously or following a request, the connection procedure is restarted (see 6.2).
The following figure shows disconnection procedure, followed by reconnect from the distributed unit.

Figure 6.4‑1: Disconnection

## Connection Supervision
If connection supervision is wanted, a Sign of Life Timer Packet can be sent to the object to force it to send periodic packets (Sign of Life Packet) to ensure that the connection is “alive”. If a packet is not sent or received in a timely fashion after having been requested, both ends should close the connection.
If a concentrator is used as per chapter 6.7, it is a good idea to send this packet do the concentrator instead of each on it.
## Diagnostics and Maintenance
It is assumed that most diagnostics and maintenance functions on distributed units are implementation specific. They will be performed outside of this protocol, using secure standard TCP/IP services, such as SFTP, SSH or HTTPS. Only generic maintenance functions, essential to the functionality of the system, have been included in the packet descriptions below.
## Using a concentrator for objects
In most instances, it would be economically unsound – for various reasons – to implement each point, input, output and so on as units on it own. There would be a lot of units on the network.
In this case a “concentrator” unit can be used. The concentrator unit may not have a name in the system per se – but it needs to have a unique identifier nonetheless. For example, this could be a numeric identifier that only the concentrator and the software it connects directly to are aware of. The TCC does then not need to know this identifier. RXID_OBJECT would then be the string representation of that numeric identifier.
# PACKET DEFINITIONS
## Packet Overview

Packet identity	Packet name	Message Direction
1	Connection Request Packet	From Object controller to TCC
2	Connection Response Packet	From TCC to Object Controller
3	Disconnect Packet	Bidirectional
4	Acknowledgement Packet	Bidirectional
5	Application Data Packet	Bidirectional
6	Reset Controller Packet	From TCC to Object Controller
7	Request Status Packet	From TCC to Object Controller
8	Sign of Life Timer Packet	From TCC to Object Controller
9	Local Release Packet	From TCC to Object Controller
10	Throw Points Packet	From TCC to Object Controller
11	Set Derailer Packet	From TCC to Object Controller
12	Set Level Crossing Packet	From TCC to Object Controller
13	Set Output Packet	From TCC to Object Controller
14	Set Electrical Points Lock Packet	From TCC to Object Controller
15	Controller Status Packet	From Object controller to TCC
16	Alarm Packet	From Object controller to TCC
17	Points Status Packet	From Object controller to TCC
18	Derailer Status Packet	From Object controller to TCC
19	Level Crossing Status Packet	From Object controller to TCC
20	Input Status Packet	From Object controller to TCC
21	Electrical Points Lock Status Packet	From Object controller to TCC
22	Output Status Packet	From Object controller to TCC
23	Sign of Life Packet	From Object controller to TCC
41	Request Site Data Packet	From Object controller to TCC
42	Sign of Life Packet	From TCC to Object controller

## Connection Management
### Connection Request Packet
To be sent by a distributed node to initialise the connection (see 6.2). The layout of this packet must be constant regardless of protocol version.
Variable	Length	Comment
RNID_PACKET	1	1
RL_PACKET	1	Variable
RM_ACK	1	0
RM_PROTOCOL_VERSION	2	Protocol version
RXID_SITE_DATA_VERSION	Variable	Site data version

### Connection Response Packet
Variable	Length	Comment
RNID_PACKET	1	2
RL_PACKET	1	5
RM_ACK	1	0
RM_PROTOCOL_VERSION	2	Protocol version

 To be sent in response to a Connection Request Packet (see 6.2). The layout of this packet must be constant regardless of protocol version.
### Disconnect Packet
To be sent when disconnecting (see 6.4). The layout of this packet must be constant regardless of protocol version.
Variable	Length	Comment
RNID_PACKET	1	3
RL_PACKET	1	5
RM_ACK	1	0
RQ_DISCONNECT	2	Reason for disconnection

### Acknowledgement Packet
Sent in response to any packet, requesting acknowledge (see 6.3).
Variable	Length	Comment
RNID_PACKET	1	4
RL_PACKET	1	5
RM_ACK	1	Packet instance identity, copied from received packet
RQ_ACK	2	Acceptance, or reason for rejection

### Sign of Life Timer Packet
Sent from TCC to OC to change frequency of Sign of Life messages
Variable	Length	Comment
RNID_PACKET	1	8
RL_PACKET	1	5
RM_ACK	1	Packet instance identity for acknowledge
RT_INTERVAL	2	Frequency of Sign of Life messages

### Sign of Life Packet
Sign of Life message from OC to TCC.
Variable	Length	Comment
RNID_PACKET	1	23
RL_PACKET	1	3
RM_ACK	1	0

## Bidirectional packets
### Application Data Packet
Application specific information.
Variable	Length	Comment
RNID_PACKET	1	5
RL_PACKET	1	Variable
RM_ACK	1	Packet instance identity for acknowledge, if required
RNID_XUSER	2	Identifies the receiver of the message
Other data, depending on RNID_XUSER	Variable

## Commands From TCC to Object Controller
### Configuration
#### Site Data Packet
Sent from server in order to reconfigure remote computer.
Variable	Length	Comment
RNID_PACKET	1	42
RL_PACKET	1	Variable
RM_ACK	1	Packet instance identity for acknowledge
data	Variable	Byte array with configuration data.

### All Types of Objects
#### Reset Controller Packet
Sent to command a reset of an OC or a concentrator, e.g. to resolve certain error states.
Variable	Length	Comment
RNID_PACKET	1	6
RL_PACKET	1	3
RM_ACK	1	0

#### Request Status Packet
Sent to request status information from an object. The distributed unit will respond by sending relevant status packet (see 7.5). If the packet is sent to a concentrator (see 6.1.3.1), status information is requested from all objects connected to the concentrator.
Variable	Length	Comment
RNID_PACKET	1	7
RL_PACKET	1	3
RM_ACK	1	0

#### Local Release Packet
Sent to allow or revoke local control of an object which supports this function (i.e points, derailer or level crossing barrier).
Variable	Length	Comment
RNID_PACKET	1	9
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_RELEASE_COMMAND	1	Requested state

### Points
#### Throw Points Packet
Sent to request a change of points direction.
Variable	Length	Comment
RNID_PACKET	1	10
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_POINTS_COMMAND	1	Requested direction of points

### Derailer
#### Set Derailer Packet
Sent to request a derailer to be passable or non passable.
Variable	Length	Comment
RNID_PACKET	1	11
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_DERAILER_COMMAND	1	Requested state of derailer

### Level Crossing
#### Set Level Crossing Packet
Sent to request a level crossing to open or close.
Variable	Length	Comment
RNID_PACKET	1	12
RL_PACKET	1	7
RM_ACK	1	Packet instance identity for acknowledge
RQ_LEVEL_CROSSING _COMMAND	1	Requested state of level crossing barrier
RT_DELAY	2	Preparation time
RNID_TRACK	1	Which track the order concerns

### Generic Output
#### Set Output Packet
Sent to request a change of output state.
Variable	Length	Comment
RNID_PACKET	1	13
RL_PACKET	1	6
RM_ACK	1	Packet instance identity for acknowledge
RQ_OUTPUT_COMMAND	1	Requested state of output
RT_DURATION	2	Max time before returning to default state (off)

### Electrical Points Lock
#### Set Electrical Points Lock Packet
Sent to request a change of output state.
Variable	Length	Comment
RNID_PACKET	1	14
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_POINTS_LOCK_COMMAND	1	Requested status of electrical point lock

### Other Types of Objects
The architecture overview in ref. [3] shows interfaces to several additional object types, i.e.
- Adjacent Interlocking
- Points Heater
- Track Circuit
Commands to these object types will be made through Generic Output signals.
## Status Reports from Object Controller to TCC
### Configuration
#### Request Site Data Packet
Sent from object controller unit in order to request site data configuration.
Variable	Length	Comment
RNID_PACKET	1	41
RL_PACKET	1	3
RM_ACK	1	Packet instance identity for acknowledge

### All Types of Objects
#### Controller Status Packet
Sent from a concentrator to inform TCC of a change of operational state in the OC.
Variable	Length	Comment
RNID_PACKET	1	15
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_CONTROLLER_STATE	1	Status of controller. Unavailable, Restarting or Operational

#### Alarm Packet
Sent to inform TCC of errors or other events in the OC, the object or the concentrator.
Variable	Length	Comment
RNID_PACKET	1	16
RL_PACKET	1	15
RM_ACK	1	Packet instance identity for acknowledge
RQ_ALARM_CODE	2	Code for alarm
RN_ALARM_LEVEL	1	Severity level of alarm
RQ_ALARM_STATE	1	Condition present/cleared, or transient event
RN_PAR_1	4	Informational parameter. Interpretation is dependant on RQ_ALARM_CODE
RN_PAR_2	4	Informational parameter. Interpretation is dependant on RQ_ALARM_CODE

### Points
#### Points Status Packet
Sent when OC detects a change of status, or on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	17
RL_PACKET	1	7
RM_ACK	1	Packet instance identity for acknowledge
RQ_POINTS_STATE	1	Current direction/position of points
RQ_RELEASE_STATE	1	Current local release state of object
RT_OPERATION	2	Duration of most recent operation

### Derailer
#### Derailer Status Packet
Sent when OC detects a change of status, or on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	18
RL_PACKET	1	7
RM_ACK	1	Packet instance identity for acknowledge
RQ_DERAILER_STATE	1	Current state of derailer
RQ_RELEASE_STATE	1	Current local release state of object
RT_OPERATION	2	Duration of most recent operation

### Level Crossing
#### Level Crossing Status Packet
Sent when OC detects a change of status, or on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	19
RL_PACKET	1	8
RM_ACK	1	Packet instance identity for acknowledge
RQ_LEVEL_CROSSING _STATE	1	Current state of object
RQ_RELEASE_STATE	1	Current local release state of object
RT_OPERATION	2	Duration of most recent operation
RQ_LEVEL_CROSSING_FAULT	1	Current fault state of object

### Generic Input
#### Input Status Packet
Sent when OC detects a change of status, or on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	20
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_INPUT_STATE	1	Current state of Input

### Electrical Points Lock
#### Electrical Points Lock Status Packet
Sent when OC detects a change of status, or on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	21
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_POINTS_LOCK_STATE	1	Current status of electrical points lock

### Generic Output
#### Output Status Packet
Sent on request from TCC.
Variable	Length	Comment
RNID_PACKET	1	22
RL_PACKET	1	4
RM_ACK	1	Packet instance identity for acknowledge
RQ_OUTPUT_ STATE	1	Current state of output

### Other Types of Objects
The architecture overview in ref. [3] shows interfaces to several additional object types, i.e.
- Adjacent Interlocking
- Points Heater
- Track Circuit
- Tongue Detection Contact
Status of these object types will be acquired through Generic Input signals.
# VARIABLE DEFINITIONS
## RL_MESSAGE
Name	Message length
Description	RL_MESSAGE indicates the length of the message in bytes, including all packets and all variables defined in the message header.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 bytes	7	250	Number of bytes
Special/Reserved Values

## RL_PACKET
Name	Packet length
Description	RL_PACKET indicates the length of the packet in bytes, including all variables of the packet header.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 bytes	6	240	Number of bytes
Special/Reserved Values

## RM_ACK
Name	Identity for acknowledgement
Description	Identifies the packet instance for acknowledgement. (See 6.3)
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 bytes	0	255	Implementation specific
Special/Reserved Values	0	No acknowledgement is expected

## RM_PROTOCOL_VERSION
Name	Version identifier
Description	Indicates the protocol version. (See 4)
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	1	65535	Numbers
Special/Reserved Values

## RN_ALARM_LEVEL
Name	Alarm level
Description	Indicates severity level of alarm.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	255	Increasing number indicates increasing severity.
Special/Reserved Values

## RN_PAR_1
Name	Information parameter
Description	Interpretation of this parameter is dependant on RQ_ALARM_CODE
Length of variable	Minimum Value	Maximum Value	Resolution/formula
4 bytes	-2147483648	+2147483647	Numbers
Special/Reserved Values

## RN_PAR_2
Name	Information parameter
Description	Interpretation of this parameter is dependant on RQ_ALARM_CODE
Length of variable	Minimum Value	Maximum Value	Resolution/formula
4 bytes	-2147483648	+2147483647	Numbers
Special/Reserved Values

## RNID_PACKET
Name	Packet identifier
Description	Used in each packet, allowing the receiving equipment to identify the data, which follows.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	1	65535	Number
Special/Reserved Values		See list in section 7.1

## RNID_TRACK
Name	Track address
Description	Addresses a specific track in a Set Level Crossing command
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	0	255
Special/Reserved Values	0	Master object

This variable allows a Close or Open after Passage command to be directed to one out of several parallel tracks through the level crossing. The distributed unit can then control signals and check track detection devices accordingly, and keep track of multiple trains I the level crossing.
## RNID_XUSER
Name	User identifier
Description	Identifies the receiver of an Application Data Packet
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	1	65535	Number
Special/Reserved Values	1	Bombardier Transportation application

## RQ_ACK
Name	Acknowledgement
Description	Indicates acceptance or rejection of a received package
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	0	6
Special/Reserved Values	0 / 1 / 2 / 3 / 4 / 5 / 6	Accepted / Rejected by receiver, unspecified reason / Unknown receiver identity / Unknown packet identifier / Wrong packet identifier for this receiver / Unknown state requested / Object locally released

## RQ_ALARM_CODE
Name	Alarm code
Description	Indicates the reason for an alarm.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	1	65535
Special/Reserved Values		The set of possible alarm codes is implementation specific. TCC must allow the interpretation of the alarm codes to be configurable.

## RQ_ALARM_STATE
Name	Alarm status
Description	Indicates status of alarm.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	3
Special/Reserved Values	1 / 2 / 3	Alarm condition is active / Alarm condition is not present / Transient event

## RQ_CONTROLLER_STATE
Name	Controller status
Description	Indicates status of controller.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	3
Special/Reserved Values	1 / 2 / 3	Unavailable / Restarting / Operational

## RQ_DERAILER_COMMAND
Name	Derailer state
Description	Requested status of derailer.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	Passable / Non passable

## RQ_DERAILER_STATE
Name	Derailer state
Description	Indicates current status of derailer
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	4
Special/Reserved Values	1 / 2 / 3 / 4	Passable / Non passable / Moving / Out of Control

## RQ_DISCONNECT
Name	Reason for disconnection
Description	Information about the reason for disconnection
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 byte	1	5
Special/Reserved Values	1 / 2 / 3 / 4 / 5	Wrong site data version / Wrong protocol version / Wrong sender identity / Wrong receiver identity / Unit closing down

## RQ_INPUT_STATE
Name	Input state
Description	Indicates state of input.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	3
Special/Reserved Values	1 / 2 / 3	On / Off / Undefined

## RQ_LEVEL_CROSSING _COMMAND
Name	State of level crossing
Description	Requested level crossing action.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	5
Special/Reserved Values	1 / 2 / 3 / 4 / 5	Open now (local track automation deactivation) / Open after passage / Close / Activate Reduced Automatic mode / Deactivate Reduced Automatic mode

The Open after passage command will not cause the level crossing to open immediately, but when track detection devices indicate that the train has passed.
In Reduced Automatic mode, opening and closing will be controlled by the track detection indications directly. To be used for Special Train Route and in shunting.
The Close command will initiate a Preparation order to the level crossing equipment, to be followed by an Activation order after the specified RT_DELAY.
## RQ_LEVEL_CROSSING_FAULT
Name	Level crossing fault state
Description	Current fault state of object
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	5
Special/Reserved Values	1 / 2 / 3 / 4 / 5	No fault / Operational fault / Safety fault / Operational and Safety fault / Fault signal(s) out of control

## RQ_LEVEL_CROSSING _STATE
Name	State of level crossing
Description	Indicates current level crossing status.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	6
Special/Reserved Values	1 / 2 / 3 / 4 / 5 / 6	Open / Prepared for activation / Activated for closing / Closed / Opening / Out of control

## RQ_OUTPUT_COMMAND
Name	Output state
Description	Indicates requested state of output.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	On / Off

## RQ_OUTPUT_ STATE
Name	Output state
Description	Indicates current state of output.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	On / Off

## RQ_POINTS_COMMAND
Name	Direction of points
Description	Requested direction of points.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	A train facing the points will be diverted to the right / A train facing the points will be diverted to the left

## RQ_POINTS_LOCK_COMMAND
Name	Status of electrical point lock
Description	Requested status of electrical Point Lock.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	Unlock / Lock

## RQ_POINTS_LOCK_STATE
Name	Status of electrical point lock
Description	Indicates current status of electrical Point Lock.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	4
Special/Reserved Values	1 / 2 / 3 / 4	Locked Right / Locked Left / Unlocked / Out of control

## RQ_POINTS_STATE
Name	State of points
Description	Indicates current direction of points.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	4
Special/Reserved Values	1 / 2 / 3 / 4	Right / Left / Moving / Out of control

## RQ_RELEASE_COMMAND
Name	Release of object for local control
Description	Requested local release state of an object.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	2
Special/Reserved Values	1 / 2	Released for local control / Central Control

## RQ_RELEASE_STATE
Name	Release of object for local control
Description	Local release state of an object.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
1 byte	1	3
Special/Reserved Values	1 / 2 / 3	Released for local control / Central Control / Unknown

## RT_DELAY
Name	Preparation time
Description	Indicates time before level crossing shall be activated (begin to close).
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	1	65535	0.1 Seconds
Special/Reserved Values	0	Waiting time not yet known. Stay in prepared mode until warning time is updated by a new command.

## RT_DURATION
Name	Output signal duration time
Description	Max time to keep an output signal on, if no new command is received.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	0	65535	0.1 Seconds
Special/Reserved Values	0	Constantly on

## RT_INTERVAL
Name	Frequency of Sign of Life messages
Description	For altering the periodicity of Sign of Life messages. Ordered interval remains in effect until superseded by a new Sign of Life Timer packet, or until the communication is disconnected.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	0	65535	0.1 seconds
Special/Reserved Values	0	No application layer Sign of Life messages to be sent

## RT_OPERATION
Name	Duration of object operation
Description	Indicates the duration of the most recent object movement.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
2 bytes	0	65535	0.1 Seconds
Special/Reserved Values	0	Unknown or not applicable

## RXID_OBJECT
Name	Object identifier
Description	Indicates the identity of the object.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
Max. 80 bytes			Null terminated UTF-8 string
Special/Reserved Values		See 6.1.3.1.

## RXID_SITE_DATA_VERSION
Name	Site data version
Description	Identifies the version, current or requested, of the site data in a distributed unit.
Length of variable	Minimum Value	Maximum Value	Resolution/formula
Max. 40 bytes			Null terminated UTF-8 string
Special/Reserved Values

# CONFIGURABLE PARAMETERS
## Generic Application Data
These parameters may be defined asymmetrically, i.e. one value applies to the TCC side and another to the distributed units.
### Network Layer
Port number
Port for which to open a listening socket (TCC only).
### Application Layer
- Application Connect Timer
  Specifies the time limit within which a Connect Response message is expected in response to a previously sent Connect Request message.
- Acknowledgment Timer
  Specifies the time limit within which an acknowledgment is expected for a message with RM_ACK > 0.
- Connection Attempt Interval
  Specifies the interval after which a failed connection attempt is repeated.

## Specific Application Data
These parameters are specified individually for each node. The TCC must also have access to configuration parameters for all connected nodes. The distributed nodes must also have access to configuration parameters for the TCC.
#### Application Layer
Local Identifiers
Text strings, which uniquely identifies all units (objects, OCs and concentrator) served by the local node.
Restriction: To follow rules in 6.1.3.1.